## Slide 1: Home Networking
Seo, Dae Young
(seody@kpu.ac.kr)
Fall, 2015
Chairman, OSGi Users’ Forum Korea
NGN Services Engineering House
Department of Computer Engineering,
Korea Polytechnic University

## Slide 2: Contents
Introduction
2. UPnP(Universal Plug and Play)
3. Jini
4. Havi(Home Audio Video Interoperability)
5. Other HNW Middlewares
6. OSGi(Open Services Gateway initiatives)
References

## Slide 3: 1. Introduction

## Slide 4: Introduction - Middleware
홈네트워크 구현의 문제점
  한 종류의 네트워크로 모든 기기들의 특성 만족은 불가
    유선
      새로 케이블을 구축
        비용 추가
      전화선 혹은 전력선 사용
        대역폭 제한(Limited Bandwidth)
    무선
      전송거리, 접속 노드 수의 부족, 상호 간섭
  해결책
    다양한 홈 네트워크를 혼합 사용
  다양한 홈네트워크 사용시 요구사항
    이종 네트워크 간의 제어/모니터링이 가능하여야 함
    데이터의 흐름이 투명하여야 함
    사용자는 네트워크 구성에 대하여 알 필요가 없음
    서비스를 위한 응용 프로그램의 손쉬운 적용
  => 미들웨어 요구 등장!

## Slide 5: Introduction - Middleware
App #1
App #2
App #3
App #N
Home Network Application
- 원격 분석
  - 가전제품의 제어
  - 홈쇼핑
  - 인터넷/파일 공유
IEEE
1394
USB
Home
PNA
Blue
Tooth
Home Network
Middleware Solutions
( UPnP, Jini, HAVi)
...
Companion
Protocols
Interface
HTTP / TCP / IP
Home Network
Middleware
Distributed
Home Network
Applications
Messaging
...
다양한 인터페이스 기술
  IEEE1394, USB,
  Ethernet, HomePNA,
  HomeRF, Wireless-LAN, Bluetooth,
  Powerline
?
GAP

## Slide 6: Introduction - Middleware
Middleware of Computer
  각기 분리된 두 개의 프로그램 간의 매개 역할을 하거나 연합시켜 주는 프로그램
  예: 데이터 베이스 접근을 위한 미들웨어
What is Middleware?
  사용자가 H/W 및 O/S에 무관하게 일관성 있는 프로그램을 만들게 하는 프로그램
  사용자에게는 일관성 있는 API를 제공하지만 내부는 적용 H/W 및 O/S에 맞도록 제공
Major Home Network Middlewares
  HAVi, Jini, UPnP, OSGi, etc.

## Slide 7: Home Network Technologies

## Slide 8: 2. UPnP

## Slide 9
UPnP
SUN 의 JINI에 대응하기 위하여 MS에서 만든 Middleware Standard
PnP 확장 개념
Based on existing technologies(IP, Http, XML)
Node Category
  Control Point
  Controlled Device
  UPnP Bridge
  Legacy Device

## Slide 10
UPnP Network Architecture
IP Network
Non-IP Network
Control point
(Laptop)
Control point
(PDA or Smart Phone)
Non-UPnP 기기
(CEBus Refrigerator)
Non-UPnP Device
(X10 Microwave Oven)
Native Device
(UPnP VCR)
UPnP Bridge

## Slide 11
UPnP Protocol Stack
IP
UDP
TCP
HTTPMU
(discovery)
HTTPU
(discovery)
HTTP
HTTP
(description)
SSDP
GENA
SOAP
Defined by UPnP Forum Working Committee
Defined by the UPnP vendor
UPnP device architecture

## Slide 12
UPnP
UPnP 동작
  Addressing
  Discovery
  Description
  Control
  Eventing
  Presentation

## Slide 13: UPnP : Addressing
Description
Server
Discovery
Server
Description
Document
Service
State Table
Presentation
Server
Service
Presentation
Server
Service
Event
Source
Control
Server
Root Device
Device
Event
Subscription
Server
Control URL
Presentation URL
Description URL
Event Sink URL
Event Subscription URL

## Slide 14: UPnP : Discovery(1)
SSDP Announcement
  Online
  Offline
Device
Device
Device
Device
Device
Device
Hello!
Bye!
HTTPMU Request
HTTPMU Request

## Slide 15
UPnP : Discovery(2)
Discovery
Discovery
M-Search * HTTP/1.1
HOST: 239.255.255.250:1900
MAN: “ssdp:discover”
…
ST: upnp:dtype:VCR
VCR
TV
Control Point
HTTPMU Request
SSDP Search Request : M Search
  Header specifies search criterion value
    Device type
    Service type
    Unique device name

## Slide 16
UPnP : Discovery(3)
Discovery
Discovery
HTTP/1.1 200 OK
…
LOCATION:
http://vcr:2000/desc.xml
VCR
TV
Control Point
HTTP Response
SSDP Search Response
    Device must send unicast response
    Must respond only to matching search request
    Response contains URL to device’s description document

## Slide 17
UPnP : Discovery(4)
UDP
UDP
Discovery Client
(could be part of CP UI)
CP
User
Interface
Discovery Server
HTTP Server
SSDP
Options Request (HTTPU or HTTPMU)
Announce
Options Response
Announce
Options Request
Options Response
Control Point
Controlled Device

## Slide 18
UPnP : Description(1)
Description
GET desc.xml HTTP/1.1
HOST: vcr:2000
HTTP/1.1 200 OK
…
CONTENT-TYPE: text/xml
…
<?xml version=“1.0”?>
… description document …
Control Point
VCR
Accessing Description
  URL specified in search response
  Description server must listen for HTTP Get request
    Must send HTTP response containing description document in the body

## Slide 19
UPnP : Description(2)
TCP
TCP
Description Doc Client
(XML parser for document)
CP
User
Interface
Description Doc
Server
HTTP Server
GET
OK
HTTP/1.1
Document
DB
HTTP/1.1
OK
GET
UCP description document client will parse the document. Document will be formatted and displayed in UCP UI

## Slide 20
UPnP : Control(1)
<SOAP:Envelope>
<SOAP:Header>
…
</SOAP:Header>
<SOAP:Body>
<SetVolume>
<newVolume>100</newVolume>
</SetVolume>
</SOAP:Body>
</SOAP:Envelope>
<SOAP:Envelope>
<SOAP:Body>
<SetVolumeResponse>
<return>0</return>
</SetVolumeResponse>
</SOAP:Body>
</SOAP:Envelope>
Control Request
  SOAP messages
    HTTP POST or M-POST requests
    XML body specifies action to invoke and values for argument
Control Responses
  Send SOAP response via HTTP

## Slide 21
UPnP : Control(2)
Controlled
Device
Control Point
Description
Document
Control
Server
Browser
Presentation
Browser
Control
Rehydrator
Applications
Service Definition:
Service State Table + Actions
Service Control Protocol Declaration
Service Control Protocol
Embedded
Implemented (Server)
Uploaded
SCP (Client)

## Slide 22
UPnP : Control(3)
TCP/UDP
TCP/UDP
Rehydrator
CP User
Interface
(SCP Control)
Control
Server
HTTP Server
Text/xml encoding from SCP POST / M-POST
200 OK
HTTP/1.1
SST
HTTP/1.1
SCP
200 OK
Local
Service
Text/xml encoding from SCP POST / M-POST
Generate Events
Update
SOAP
Native API
OS(Native) API

## Slide 23: UPnP : Event(1)
Subscribing
  SUBSCRIBE request sent via HTTP
  HTTP response contains new Subscribe ID
Event Server
SUBSCRIBE eventSource HTTP/1.1
HOST: vcr:4000
…
Callback:<http://ucp:923/upnp>
HTTP/1.1 200 OK
SID: uuid: …(new uuid) …
…
Control Point
VCR

## Slide 24: UPnP : Event(2)
Notifications
  Event source sends HTTP request to each subscriber
    Body contains XML fragment which specifies changed variables and new values
  Initial Notification
    Event server must send initial notification immediately for new subscription
    Must contain current values for all state variables
Sequence Number
  UPnP event must be numbered
    Sequence numbers are used for synchronization
  Event source must send a sequence number in each Notify message header
A
B
C
State Table
Control
Server
Event
Server
AB C
NOTIFY upnp HTTP/1.1
HOST: ucp:923
…
Context-Type: text/xml
<…xml fragment …>

## Slide 25
UPnP : Event(3)- Subscription
TCP/UDP
Event
Subscription
Client
UCP
User
Interface
GENA Subscribe
HTTP/1.1
TCP/UDP
Subscription Arbiter
Event Subscription
Server
NOTIFY
HTTP/1.1
Notification
Event
Source
HTTP Server
Native App
Event Sink
Rehydrator
NOTIFY
GENA Subscribe
GENA

## Slide 26
UPnP : Event(4)
Control Point
Controlled Device
Discovery
Client
Description
Client
Discovery
Server
Description
Server
Description
Document
Application
Event
Subscription
Server
Event
Source
Event
Subscription
Client
Event
Sink
Per Service
SSDP
Description
(Event Subscribe URL)
Notify(Event)
Description
(Event Sink URL)

## Slide 27: UPnP : Presentation
Presentation
  Control Point can retrieve a page from this URL
  Delivers an HTML page and provide device specific UI
Accessing Presentation
  Use HTTP GET on presentation URL specified in description documentation
Presentation
GET pres:html HTTP/1.1
HOST: vcr:3000
Control Point
@ Presentation Page
Play>>
Pause
Stop
VolumeUp
VolumeDown

## Slide 28: UPnP Standardization
UPnP 표준현황
  DLNA에서 기본으로 채택
  OSGi Provides UPnP Bundle
  Device Category
    AV
    Basic
    HA
    Networking
    Printer
    Remoting
    Scanner
  추가 서비스
    Device Security and Security Console
    QoS
  ISO/IEC 29341 (in Dec. 2008)

## Slide 29: 3. Jini

## Slide 30: Jini
Jini 소개
  마술이라는 뜻
  SUN에서 홈네트워크용 미들웨어로 개발
  JVM 위에서 동작하며 PnP지원
  Lookup 서버가 기기의 기능이나 특징을 가져오는 join 일어남
  서비스?
    사용자, 프로그램, 다른 서비스에 의해 사용될 수 있는 실체
    분산 시스템 내 서비스 구축, 탐색, 통신 사용등 방법을 제공해 서비스를 공유
      예를 들면 계산능력, 저장공간, 통신채널 등

## Slide 31: Jini : Characteristics
Jini has a highly distributed architecture.
Has a good scalability.
Reduces the cost of management for distributed systems.
Integrates all the software resources as terms of service.
Needs high-level software environment.
  JVM
  RMI
Always needs Lookup Services.
Only TCP/IP is the communication media. Other medium is not allowed at this moment.

## Slide 32: Jini System Architecture

## Slide 33: Jini System
Lookup Service : Discovery Protocol and Join Protocol
Java RMI(Remote Method Invocation) : Jini Infrastructure의 일부로서 서비스간 Communication Protocol로 RPC의 확장이며, 객체그룹 발견, 활성화, 수집하는 매커니즘도 제공한다. 또 객체간 데이터 전송, 코드를 포함한 완전한 객체 전송을 한다.
Security : 시스템의 특별한 사용자를 역추적 하기 위해 사용되는 Principal 과 서비스 접근제어를 위한 허용 리스트(ACL)가 있다.
리싱(leasing): Jini에서 서비스에 대한 접근은 리스(lease) 기반이며 일정 시간 동안의 보장된 접근이 허용된다. 그리고 배타적 리스와 비배타적 리스로 구분된다. 계속 서비스를 받고 싶으면 다시 리스를 하여야 한다.
원격 이벤트: 분산 이벤트와 원격 이벤트를 지원하며 객체들 간의 이벤트 등록 및 이벤트 정보 수신, 그리고 Java Beans에서 사용된 이벤트 모델의 확장이다.
트랜잭션: 오퍼레이션 수행이 트랜잭션 기반으로 이루어진다.

## Slide 34: Jini Overview
Network이나 Network 사용자에 영향 없이 동적으로 Join & leave 가 가능함

## Slide 35: Local Computing

## Slide 36: Jini Overview

## Slide 37: Local vs. Distributed Computing
Local Computing
  Single Address Space
  Single Platform
  Single Operating System
  Zero Network Protocols
  Single Executable File
  (maybe with many languages)
Distributed Computing
  Multiple Address Space
  Multiple Platform
  Multiple Operating Systems
  Multiple Network Protocols
  Multiple Programming Languages

## Slide 38: Jini Service
Discover
  Network Service discovers an available look-up server
j

## Slide 39: Jini Service
Join
  Network Service sends a service proxy to Look-up Server

## Slide 40: Jini Service
Discover
  Network Client discovers an available lookup server

## Slide 41: Jini Service
Lookup
  Network Client requests a service to look-up server

## Slide 42: Jini Service
Receive
  Look-up Server forwards service proxy to client if the service requested by Network client is registered in look-up server.

## Slide 43: Jini Service
Use
  Network client directly communicate with Network Service through service proxy
  Session maintained until the end of lease

## Slide 44: Jini Standardization
Jini 2.0 spec 출시
UPnP 와의 경쟁에서 열세
  SUN에서도 promotion 소극적
OSGi 의 기술적인 근간을 이루었으나 OSGi 에서 r4.0 이후 Jini를 지원하지 않음(반면 UPnP는 OSGi r2.0 부터 계속 번들 지원)
Ubiquitous 환경과 보안에 적합
  학계 쪽의 논문은 나오지만 진짜 실용적으로 채택될 지는 미지수

## Slide 45: 4. HAVi

## Slide 46: HAVi (Home Audio Video Interoperability)
HAVi 소개
  전세계 AV 시장의 70% 이상인 업체들이 뭉쳐 만든 홈네트워크 AV 용 표준
  IEEE 1394(FireWire) 위에서 작동
  홈네트워크는 분산 컴퓨팅 플랫폼으로 생각
HAVi 기기 분류
  LAV: 1394 only
  BAV: Device Discover 까지
  IAV: level 1 UI 까지
  FAV: level 2 UI 까지

## Slide 47: Characteristics of HAVi SW Architecture(1)
IEEE1394 통신매체 관리자 (CMM)
  소프트웨어 요소간에 IEEE1394 네트워크를 통해 비동기(asynchronous) 및 등시성(isosynchronous) 통신이 가능하도록 한다.
메시징 시스템
  HAVi 소프트웨어 요소간에 메시지 전달을 책임지고 있다.
레지스트리
  어떤 소프트웨어 요소를 네트워크 상의 다른 소프트웨어 요소에 위치하거나 능력과 특성을 검출하는 디렉토리 서비스 역할을 수행하고 있다.
이벤트 관리자
  이벤트 디렉토리 서비스 역할을 수행한다. 이벤트는 HAVi 소프트웨어 요소의 상태 또는 HAVi 네트워크 구성상태를 변경시킨다.
스트림 관리자
  기능적 컴포넌트 사이에서 AV 스트림의 실시간 전송을 담당한다.
자원 관리자
  액션의 스케줄링과 자원 공유가 가능하도록 한다.

## Slide 48: Characteristics of HAVi SW Architecture(2)
DCM(디바이스 제어 모듈)
  HAVi 네트워크에서 한 개 디바이스를 표현하는 소프트웨어 요소이며, HAVi 가 정의한 API로 공개되어있다. 사실은 DCM은 동적이다. 만약에 디바이스가 삽입되거나 제거될 때 해당 디바이스용 DCM은 네트워크로부터 설치되거나 제거될 필요가 있다.
FCM(기능 컴포넌트 모듈)
  각 디바이스에서 제어가능한 기능을 위한 FCM 모듈이며, 이는 DCM에 포함되어 있다. 현재 HAVi 는 튜너, VCR, AV 디스플레이, 카메라, 모뎀과 같은 기능을 위한 API 및 FCM을 정의하고 있다.
DCM 관리자
  DCM의 설치 및 제거에 대한 책임을 지고 있다.
어플리케이션
  어플리케이션은 HAVi 네트워크에서 소프트웨어 요소가 레지스트리 또는 DCM과 같은 다른 소프트웨어 요소와 통신이 가능하도록 하기 위해 스스로 알려줄 필요가 있다.
DDI(Data Driven Interaction)
  소프트웨어 요소는 아니지만, 어플리케이션 또는 DCM 사이에서 수행되는 프로토콜이다.
Havlet
  Havlet 은 디스플레이 기기의 요구에서 어플리케이션 또는 DCM으로부터 추출되는 Java 어플리케이션이다. 이는 Java가 가능한디스플레이 기기에서 수행되며 Java GUI API에 의해 DCM 또는 어플리케이션 대신에 사용자 인터페이스를 나타낼 수 있다.

## Slide 49: HAVi : Control Model
Full AV Device (FAV)
Download and execute all HAVi applications
Download and execute DCMs
Intermediate AV Device (IAV)
Ability to communicate with other HAVi Devices
Ability to execute limited applications
Offers own control services
Ability to host other known devices
Ability to host legacy devices
Base AV Device (BAV)
Offers own control information in ROM
Legacy AV Device (LAV)
Conventional devices w/ no HAVi SDD
Controller-
Capable
HAVi
Device
Controlled
HAVi
Device

## Slide 50: HAVi Device Types
FAV(Full AV Device):
  풍부한 자원을 갖고 있으며 복잡한 소프트웨어 환경을 지원한다.
  자바 런타임 환경의 출현으로 FAV가 바른 기기로부터 바이트코드를 업로드하는 것이 허용되고 제어를 위한 능력이 고급화된 것을 제공한다.
  후보제품군들: 세탑박스, DTV, 홈서버등
IAV(Intermediate AV Device):
  FAV 보다는 비교적 저렴하고 자원 측면에서 좀 더 제한적이다.
  자바 런타임 환경을 제공하지 않기에 아무 기기의 콘트롤러로서 동작할 수는 없다. 특정 기기들의 콘트롤러 지원을 제공한다.
BAV(Base AV Device)
  업로드 가능한 자바 바이트코드를 제공한다.
  HAVi 아키텍처의 어떤 소프트웨어 요소도 호스트 하지 못한다.
  업로드 가능한 바이트코드를 통하여 FAV에 의해 제어를 받던지, IAV의 네이티브 코드를 통하여 제어를 받는다.
  FAV 와 BAV 간, 또는 IAV 와 BAV 간의 통신은 HAVi 명령어와 BAV에서 사용되는 명령어 프로토콜 간에 서로 변환되어야 가능하다.
LAV(Legacy AV Device)
  HAVi 아키텍쳐를 인식하지 못하고 단순한 제어만 가능한 프로토콜을 갖고 있다.
  IAV 나 FAV를 게이트웨이로서 필요로 하고 FAV 와 LAV 간, 또는 IAV 와 LAV 간의 통신은 HAVi 명령어와 레가시 명령어 프로토콜 간에 서로 변환되어야만 가능하다.

## Slide 51: HAVi Architecture - LAV

## Slide 52: HAVi Architecture - BAV

## Slide 53: HAVi Architecture - IAV

## Slide 54: HAVi Architecture - FAV

## Slide 55: HAVi Architecture

## Slide 56: 5. Other Middlewares

## Slide 57: DLNA
DLNA(Digital Living Network Alliance)
  2003년에 결성된 DHWG(Digital Home Working Group)에서 2004년 DLNA로 개칭
  UPnP 를 기본으로 채택. 디지털 기기간 호환을 위한 가이드라인 성격

## Slide 58: HWW
HWW(Home Wide Web)
  IEEE 1394 기반
  DTV에서 화면상으로 다른 가전 기기들을 제어하는 것을 가능하게 하는 목적으로 삼성에서 개발
  2000년 CEA에서 미국표준으로 채택 (EIA-775, EIA775A)

## Slide 59: VESA 와 VHN
VESA(Video Electronics Standard Association)
  Settop Box 속 기능들을 표준화하는 목적의 표준(1995)
  초창기에는 IEEE1394를 백본망으로 채택했었으나 지금은 IP 프로토콜을 네트워크 간 통신방법으로 채택
  웹 브라우저와 웹서버들을 선택 인터페이스로 결정
VHN(Versatile Home Networking)
  VESA 홈네트워크 위원회가 홈네트워크 미들웨어 솔루션 대부분을 포함하는 VESA Home Network Spec 1.0 발표(1999)
  홈 인터넷에 접속되어 있는 모든 기기들간 통신이 가능하기 위해서 필요한 공통된 네트워크간 통신이 필요한데 이 프로토콜에는 네트워크 계층 프로토콜은 물론 네트워크 프로토콜을 사용한 통신용 프로토콜과 기기들을 네트워크 자율적으로 배치하는데 필요한 다른 프로토콜등이 이에 속함.

## Slide 60: VESA 와 VHN
  HTML을 직접 지원하는 통상적인 GUI 프록시를 통하여 사용자-기기 제어
  기기발견 query와 공유언어(계층적 XML, RPC)와 HNB 와 Interface Repository 에 기반
  네트워크 관리는 표준 CIM 사용
  사실상 UPnP를 subset 으로 함

## Slide 61: 동향
Siemens 주도로 UIC(UPnP Implementor’s Cooperation) 라는 이름으로 ISO/IEC JTC1 SC25 에 UPnP 1.0을 표준 시도
UPnP 2.0은 인증과 접근제어등의 보안기능이 추가되나 1.0과 호환 불가능
삼성전자에서 HD TV를 위한 표준인 HANA(High-Definition Audio-Video Network Association) 만들어 주도
ETRI에서 UMB(Universal Middleware Bridge) 라는 통합 미들웨어 솔루션을 개발하여 국제 표준 제안 후 공개배포
  LnCP, LonWorks, UPnP, HAVi 등이 어댑터 형식으로 Core에 장착
KETI에서 IEC TC100에 CCP(Common Communication Protocol)을 국제 표준으로 제안하여 통과됨.
  모든 기기에 새로운 계층 만들어야 하는 단점 있지만 표준 통과됨

## Slide 62: 동향
하나의 미들웨어 가능?
  이미 많은 미들웨어들 존재
  하나만의 winner는 나오기 힘듬
    아무리 UPnP가 막강하더라도 UPnP가 다루지 못하는 부분 존재함.
    차후 UPnP보다 더 나은 솔루션이 나왔을 시 채택 가능하여야 함
IEEE 1394의 성공 여부는 SCSI를 어느 정도 대체하느냐에 달렸음
OSGi 의 철학적 고뇌의 출발점

## Slide 63: 6. OSGi

## Slide 64: OSGi 배경
What’s missing?
  There are many wide area network standards
  There is no service delivery standard
  The are many in-home network standards
Standard for
service delivery
DOCSIS, DSL, ISDN, Satellite, W-CDMA…
Bluetooth, CEBus HAVi, HomePNA, HomeRF, Jini, LONWORKS, UPnP…

## Slide 65: Services Gateway?
A Web Phone
Anything running OSGi APIs!
A Cable Modem
A Dedicated RG(Residential Gateway)
A PC
A Set-top Box
A DSL Modem
An Automotive Multimedia Gateway

## Slide 66: Overview

## Slide 67: Residential Networks
PC
HPNA or Ethernet
PLC
Microwave
Air
conditioner
PDA
Note PC
FTTH CATV
ADSL SATELLITE
Etc.
Printer
Residential
Gateway
IEEE1394
DTV
DVD
Camcorder
Access Point
Information network
Automation network
Entertainment network
washer
Notes: In Residential Network, various home appliances exist like this figure.
( Digital TV, Camcoder, Printer, PC, Air conditioner etc.)
Diverse home appliances become to be connected and to constitute network. it is residential network, namely home network.
But the variety of home appliances results in that home appliances with similar features have developed their network to communicate one another.
Automation network to exchange simply control command like air is composed of conditioner, microwave, washer over power line. And lonWorks and CeBus are middleware for it.
Similarly, Information network to exchange file or image is developed for PC,and printer over home PNA, Wireless LAN, Bluetooth etc,,, UPnP and Jini are middleware for it
Also, Entertainment network to exchange multimedia data more voluminous than information data is over IEEE 1394 for digital tv, camcoder etc.
Havi is middleware for it

## Slide 68
HPNA or Ethernet
PLC
Residential
Gateway
IEEE1394
Access Point
based on HAVi
based on UPnP
based on Lonworks
Notes: Unfortunately these kinds of middleware is not interoperable one other.
Accordingly home appliance can’t know each other existence needless to say of using one other’s functions.
From the the view point of digitl tv, only DVD and Camcorder are in the residential network so that it can use only their functions.
In like manner, from the the view point of air conditioner, only microwave and washer are in the residential network so that it can use only their functions.
As a result,because of middleware’s heterogeneous, home appliances can’t utilize residential network sufficiently.
So I proposes framework to help home appliance interoperability.

## Slide 69: Changes of Service Adoption
Needs change and vary even for a single user. There are bunch of users!

## Slide 70: Value Chain
Local Area
Network
Provider
Service
Provider
Service
Aggregator
Service
Integrator
Services
Gateway
Operator
Device
Provider
Net Server
Operator
Telco/
Cable

## Slide 71: Value Chain
Service Provider: Third Party Bundle Developer
Service Aggregator
  “Manager” of a Service Cluster(s)
  Business Interface to Multiple Third Party Service Providers
  Manages Intellectual Property
Service Integrator
  Physical Integration of Bundles
  Manages API’s to TO / CO Core Services

## Slide 72
Network Server Operator
  Role of TO / CO
Service Gateway Operator
  Role of TO / CO
  May Not Be Part of Physical CPE on Premise
Device (CPE) Provider
  Gateways; I/O Devices; LAN; Appliances
  TO / CO May Brand Device as Differentiator
  Often Packaged with Service
TO / CO Value Chain

## Slide 73: Service Model
Services
Gateway
Wide Area
Network
Service 1
Service 2
Thread
Services
Client
Device
Local Area
Network
OSGi FRAMEWORK
Management
System
Standardized API

## Slide 74: History of OSGi
Started December 1998 as an initiative from Ericsson, Sun and IBM, etc.
Strongly influenced by Java Embedded Server (JES)/Nanoserver from Sun
Today very different from old JES (There is a new OSGi JES)
First regular meeting in 1999
Released spec v1.0 in May 2000
Released spec v2.0 in Oct. 2001
80+ members in Dec. 2001
Bundle Fest in Jan. 2002
OSGi Congress in Sep. 2002 (Stockholm)
Released spec v3.0 in Mar. 2003
OSGi Congress in 2003 (Dusseldorf), 2004 (Barcelona), 2005 (Paris)
Released spec v4.0 in Oct. 2005
Currently 30+ members (as of Oct 2006)
OSGi Developer Conference in March 2007 (Santa Clara)
OSGi Community Meeting in June 2007 (Munich)
Released spec v5.0 in 2012
Released spec v6.0 in 2014

## Slide 75: OSGi Standard Roadmap

## Slide 76: OSGi Alliance Members
Service/Content Providers
Infrastructure/Network Operators
Utilities
Software Developers
Gateway and Set Top Box Suppliers
Consumer Electronics
Research Institutes
Automobile Makers
Mobile Device Makers

## Slide 77: Who Was OSGi?(in ’00)
ABB Corporate Research
Adtranz
Alcatel
AMD
BellSouth
Broadband Gateways
Cablevision Systems
CCL/ITRI
Cisco Systems
Coactive Networks
Com21
Compaq
Deutsche Telekom
Domosys
e2-Home
Echelon
Electricite de France
Electrolux Home Products
emWare
Enikia
Ericsson
Espial Group
France Telecom
GateSpace
Home Director
Hewlett Packard
IBM
InfoGear Technology
Infomatec
inSilicon
Invensys Controls
Lineo
Maytag Corporation
Motorola
National Semiconductor
Nokia
Nortel Networks
Novell
Oracle
Philips
ProSyst Software
Samsung Electronics
Scenix Semiconductor
Schindler Aufzuge
Schneider Electric
ShareGate
Sharp
Siemens
SmartMove
Sonera
Sony
Sprint
ST Microelectronics
Sun Microsystems
Symbol Technologies
Telcordia Technologies
Telia
Texas Instruments
Tokyo Electric Power Company
Toshiba
US WEST Advanced Technologies
Verizon
Villa Montage Systems
Whirlpool
Yello Strom
Board of Directors members indicated in red

## Slide 78: Who Was OSGi?(2007)
Aplix Corporation,
BEA Systems
Deutsche Telekom
Electricit?de France (EDF),
Ericsson Mobile Platforms
ETRI
Harman Becker Automotive Systems GmbH,
Hitachi, LTD,
IBM Corporation,
Industrial Technology Research Institute,
NTT,
Oracle Corporation,
ProSyst Software GmbH
Red Hat
Robert Bosch Gmbh,
Samsung Electronics Co., Ltd.,
Siemens AG,
Sprint
Telcordia Technologies, Inc.,
Telefonica I+D,
Intel,
Interface21
IONA Technology
Jayway AB
KT
Makewave
Mitsubishi Electric Corporation,
Motorola, Inc.,
NEC Corporation,
Nokia Corporation,
BandXI International,
Cognos Inc.,
Compuware Corporation,
Db4objects, Inc.,
Eclipse Foundation, Inc,
Luminis,
Oki Electric Industry Co. Ltd.,
Paremus,
Vodafone Group Services Limited,
VTT Technical Research,
Centre of Finland,
Adopters

## Slide 79: Who Is OSGi?(2015)
Adobe
Deutsche Telekom
IBM
Liferay
NTT,
Oracle Corporation,
Paremus, Ltd
Eclipse Foundation, Inc,
Hitachi
Intuit Inc.
Mitsubishi Electric
NEC
Orange
Red Hat
Sagemcom SAS
Schneider Electric
Telecom Italia S.p.A
TIBCO
Unify GmbH & Co. KG
Contributing Associates
ProSyst Software
Salesforce.com
Software AG
Principal Members
Strategic Members
Cloudyle Luminis Makewave Sumitomo Electric Industries, Ltd.
Supporters
135+ members including Sumitomo Electric Industries, Ltd., and Huawei Technologies Co., Ltd

## Slide 80: OSGi Alliance Organization
BOD
CTO
Liaison Executive Committee
Expert Groups(2007)
  AEG, CPEG, VEG, (RMEG, SEG, DEG), MEG, EEG(new)
Expert Groups(2015)
  CPEG, EEG, IoT EG(new), Residential EG
  (VEG, MEG)
Working Committees
  Market Requirements, Marketing
Technical Steering Committee
Interest Groups
  Entertainment, Deployment
http//www.osgi.org

## Slide 81: OSGi Logo Policy
Logo Policy
  Similar to ‘Intel Inside’
  3 Categories
    OSGi Inside
      RG with Framework approved by OSGi
    OSGi Powered
      embedded OSGi inside
    Works with OSGi
      plug into OSGi
Mini Compliance Test
  March 2002
  Certification (R3.0)
    Dec. 2003

## Slide 82: Certified Products
  R2.0
  Samsung : Service Provider 2.0
  IBM : SMF 3.0.3
  ProSyst : mBedded Server 5.1
  GateSpace : GDSP 3.2
  Espial : Espial DeviceTop 3.1
  Acunia : Matilda 1.0
  Sun : JES 2.1
  Connected System : HubTea
  Embedded Server 1.2.1
  4DHomeNet : 4DAgent 1.0
  Atinav : aveLink Embedded Gateway 2.0
  Mitsubishi : TSUBASA
  Siemens : RIO
  R3.0
  Fraunhofer Institute for IC:
  Fraunhofer Embedded OSGi Platform
  IBM : SMF 3.7
  Samsung : Samsung Service Provider 3.1
  ProSyst : mBedded Server 5.2
  IBM : SMF 3.5.2
  Acunia : Matilda 2.0
  Siemens : RIO
  GateSpace Telematics : UbiServ
  Atinav : aveLink Embedded Gateway 3.0
  R4.0
  Makewave Knopflerfish Pro 2.0
  ProSyst Software mBedded Server 6.0
  Eclipse Equinox 3.2
  Samsung OSGi R4 Solution
  KT OSGi Service Platform (KOSP) 1.0
  HitachiSoft SuperJ Engine Framework 3.0

## Slide 83: Overview of OSGi Technology
Operation
  Framework
    Manage bundles
      Framework can install, update, and uninstall Bundles
      Bundles can be started and stopped
    Provides a method to share services
    Supports a package sharing
  Bundle
    A Jar file containing
      Java Classes
      Manifest with information about bundle
    Can also cat like a DLL (shared library)
    Bundle states
      Installed/Uninstalled
      Resolved
      Starting/Stopping
      Active

## Slide 84: Bundle State Transitions

## Slide 85
The Framework
Framework
Bundle A
{ }
Bundle B
{ }
Bundle C
{ }
Install A
start
Events: register
Events: install

## Slide 86
The Framework
Framework
Bundle A
{ }
Bundle B
{ }
Bundle C
{ }
uninstall
stop
Events: unregister
Events: uninstall

## Slide 87: Dependency Management
When a bundle is stopped, it is cleaned up
  Registered services are removed
  References to other services removed
Bundles can be notified when a service they depend on is unregistered
Class path dependencies are managed
Model will allow long running applications with dynamic software updates

## Slide 88: Installing a Bundle
Bundle A
( Java class,
Html file ,
manifest file
Etc.)
Bundle context
Framework
1) InstallBundle (locationString)
3) Create
Bundle object
A Bundle
Object
Check bundle is not already installed using location String
2) Obtain bundle’s contents (location or inputStream)
Allocate associated resources( bundle unique identifier, storage area etc..)

## Slide 89: Installing a Bundle(2)
Framework
A Bundle
Object
RESOLVED
Bundle A
( Java class,
Html file ,
manifest file
Etc.)
4) Resolve classpath & native code dependency
(referring manifest file)
5) Broadcast BundleEvent.INSTALLED

## Slide 90: Resolving a Bundle
Classpath dependencies
  Path to library in JAR format
Native code dependencies
  Native Code and environment
Package dependencies
  Export & import packages
  Whole package export is not recommended
  Export & import services
Classpath dependencies
  Path to library in JAR format
Native code dependencies
  Native Code and environment
Package dependencies
  Export & import packages
  Whole package export is not recommended
  Export & import services

## Slide 91: Resolving a Bundle(2)
Classpath dependencies
  Path to library in JAR format
Native code dependencies
  Native Code and environment
Package dpendencies
  Export & import packages
  Whole package export is not recommended
  Export & import services
Bundle-DocURL: http://www.servicetango.org/org/
servicetango/service/log
Bundle-Name: log
Bundle-ContactAddress: emorning@mediaone.net
Bundle-Classpath: com/sun/jes/http/servlet.jar
Bundle-NativeCode: http.DLL; osname=Win95;
processor=x86; language=en, http.so; osname=Solaris;
processor=sparc
Export-Package: org.osgi.service.log
Import-Package: javax.servlet ; specification-version="2.0"
Export-Service: org.osgi.service.log.LogReaderService
Bundle-Description: ServiceTango Log Service
Class dependency
Native code dependency
Package dependency
Export service

## Slide 92: Starting a Bundle
Classpath dependencies
  Path to library in JAR format
Native code dependencies
  Native Code and environment
Package dependencies
  Export & import packages
  Whole package export is not recommended
  Export & import services
Bundle context
Framework
A Bundle
Object
Bundle.start
Create Bundle context
Bundle A
( Java class,
Html file ,
manifest file
Etc.)
RESOLVED
1) Check bundle status
STARTING (1)
Activator.start
2) Invoke bundle’s activator start method
A Bundle :
STARTED
3) Record A bundle status started
ACTIVE(3)
4)Broadcast Bundle Event. STARTED

## Slide 93: Stopping a Bundle
Classpath dependencies
  Path to library in JAR format
Native code dependencies
  Native Code and environment
Package dependencies
  Export & import packages
  Whole package export is not recommended
  Export & import services
Bundle context
Framework
A Bundle
Object
Bundle.start
Create Bundle context
Bundle A
( Java class,
Html file ,
manifest file
Etc.)
RESOLVED
1) Check bundle status
STARTING (1)
Activator.start
2) Invoke bundle’s activator start method
A Bundle :
STARTED
3) Record A bundle status started
ACTIVE(3)
4)Broadcast Bundle Event. STARTED

## Slide 94: Bundle Activator Interface
To perform specific tasks when a bundle is started or stopped(recommended)
Start
  Allocate resources
  Register services
Stop
  Release resources
  Unregister services

## Slide 95: Updating a Bundle
Bundle A
( Java class,
Html file ,
manifest file
Etc.)
Bundle context
Framework
1) Bundle.update
A Bundle
Object
2) Back up Bundle’s JAR file
INSTALLED
New Bundle A
( Java class,
Html file ,
manifest file
Etc.)
ACTIVE
INSTALLED(3)
3) Install New version Bundle
4)Broadcast BundleEvent.UPDATED

## Slide 96: Updating a Bundle(2)
Update Process
  Succeed
    Broadcast UPDATE Event
    Resume bundle ( new version)
  Failed
    Revert to old version
    Resume bundle ( old version)
    Throw a BundleException

## Slide 97: Uninstalling a Bundle
Bundle context
Framework
1) uninstallBundle ()
A Bundle
Object
2)Broadcast BundleEvent.UNINSTALLED
UNINSTALLED (2)
ACTIVE
3)Release persistent resource of A bundle

## Slide 98: OSGi Term - Service
A service is an object registered by a bundle to be used by other bundles
The specification of a service is a Java interface
Different bundles (read vendors) can implement the same interface
Implementation is indistinguishable for users
The OSGi defines a standard set of services

## Slide 99: Service - Overview
Java classes performing functionality
  Interface & implementation separated
Service Registry
  mapping set ( service, implementation )
  Simple query mechanism ( LDAP ) : service registered with a set of properties
Configurable
  getConfiguration Object

## Slide 100: Events
Three kinds of service
  ServiceEvent : delivered synchronously
    Registration, unregisteration, property changes
  BundleEvent
    Changes in the lifecycle of bundles
  FrameworkEvent
    Framework starting or errors
Corresponding Listener interface
  ServiceListener
  BundleListener
  FrameworkListener

## Slide 101: OSG Market Trends
Growth of Internet Devices in the U.S.

## Slide 102: OSG Market Analysis
Security Service Market
  OSG Service Framework would substitute for existing security systems
Remote Home Healthcare Market
  Over 27 mil elderly citizens in USA
  Ease of mind

## Slide 103: Scenarios and Services for Different Market Segments
  Communication
    Firewall, Multiple PC Internet access, IP Telephony, Telephony, VPN services
  Energy and Utility Service
    AMR, Energy Mgmt, …
  Automation and Control Service
    Remote electrical outlet control
  Security Service
    Remote (video) surveillance, remote entry control
  Remote Healthcare Service
    Diagnostic and vital function monitoring
    (Audio/video) surveillance
    Remote entry control

## Slide 104: OSGi Functional Requirement
Industry Specific Functions
  Communication Services Module
    IP address issues
  Energy/Utility Services Module
    Data time stamping issues
  Automation/Control Service Module
    Scheduling issues
  Security Service Module
    Alarming issues

## Slide 105: OSGi Functional Requirement
Industry Specific Functions (Continued)
  Entertainment Service Module
    AV issues
  Home Care Service Module
    Emergency alert issue
  Point of Sale Service Module
    Credit card authorization issues
  Application Services Module
    Remote maintenance access issue

## Slide 106: Service Model
Personal Portal
Thread Services (Scheduling. Shopping, Address Book)
Internet Access (any ISP)
Communications (Unified Communications)
Home Networking/Gateway/Security
Service Mgmt. /Billing/Help Desk/etc.
Core Services
Home Control
Information Management
Entertainment
Internet Portal
Work at Home
Gaming
The Future
The Future
The Future
Channels

## Slide 107: Market Research Clusters
Home Management
  List Management
  Calendar
  Address Book
Information Retrieval
Entertainment
  Video/Music on Demand
  Games on Demand
  Cable Package
Home Control
  Home System Management
  Home System Alerting
  Home Entry
  Remote Appliance Controls
Telephony
  Additional Lines (VoIP)
  Video Conferencing
  Custom Routing
  Personalized Mailboxes
  Alerting & Chat

## Slide 108: Advantage of OSGi
Platform independence
Application independence
Security
Various Services
Various local network technologies
Various device access technologies
Interoperability with other standards

## Slide 109: OSGi Markets and Solutions
Enterprise
  Siemens
Open Source
  Apache Felix http://incubator.apache.org/felix
  Eclipse Equinox http://www.eclipse.org/equinox
  Knopflerfish http://www.knopflerfish.org
Mobile
  JSR 232. Nokia and Motorola
Automotive Electrons
  BMW, Bombardier, Ertico GST, Groeneveld IT B.V., mm-lab, Pilotfish, Siemens, Volvo, Wind River
SmartHome
  Blekinge Tekniska, BSH, Cisco, E2-Home, eNeo, EDF(M@jordom), Infinis, IntercomponentWare, Philips iPronto, Portus, Raum Computer, Siemens Med and Prosyst, Siemens Belgium

## Slide 110: OSGi Adoption Cases
Siemens VDO Top Level Architecture
  Since Q4/2003 the new BMW 5-series and 6-series proposes a Top Level Architecture (TLA) based system worldwide including:
    Entertainment (CD, TV, Logic 7 amplifier)
    Communication (Bluetooth phone, SMS)
    GPS Navigation (Whole Europe on DVD)
    Telematics (BMW Assist, BMW Online, E-Call)
    Car Configuration (Head-Up Display, Car locking)
    Climate Control
(By OSGi Alliance)
(By OSGi Alliance)

## Slide 111: OSGi Adoption Cases
Telefònica – Hogar.es Architecture
Corporate systems
(provision, activation, billing,
failure management, etc.)
Automatization Network
Entertainment Network
Data Network
Residential Consumers
Gateway management interface
Services aggregation interface
Corporative systems interface
Service Providers
UNED University /
Telefonica
Hospital Clínico San Carlos I / Telefonica
Telefónica
Services:
Home Care
E-learning
Surveillance,
Multimedia,
Information
Service Aggregator
Remote Manager
(By OSGi Alliance)

## Slide 112: Future Prospect of OSGi
OSGi as the value chain integrator
Key Framework for Platform Leadership/Ownership in Convergence era
Will continue to be business model neutral and policy neutral
Will be the “bridges” to seamless integration for mobile devices
HOME
AUTO
OFFICE
MOBILE
Service
Providers
Content &
Media Providers
Application
Developers
Manufacturers
IT Providers
Cost
Savings
Increased
Speed to Market
Strategic
Market
Differentiation
Increased
Revenue
Consolidated
Support
OSGi Alliance
INPUT AND ACCESS ACROSS THE ENTIRE VALUE CHAIN
(By OSGi Alliance)

## Slide 113: OSGi Users’ Forum Korea
Charter
  Promotion of OSGi service platform in Korea
  Raise of business effectiveness in vertical market and related industries
  New business model
  Business Collaborations: Home Network, Telematics, and Mobile Service
  Exchange and share experiences and views of OSGi
History
  2005. 3.23: Founded by 24 members
  2005. 5.23: 1st Seminar
  2006.10 : 2nd Seminar
  2007.10 :3rd Seminar
Wareplus
Veloxsoft
WiSEGRAM
KOTBA
TTA KETI
Kangnung National Univ.
ComStar Confitech DIYCAD.com Hyundai MOBIS
IBM Korea ISET
Lucent Technologies Korea
NEMOsoft
Seoul Commtech
UBIST

## Slide 114: References
[1] ISO/IEC, “Architecture of the Residential Gateway.” ISO/IEC JTC1 SC25 WG1 N912
[2] Zahariadis B. Theodore, “Home Networking Technologies and Standards”, Artec, 2003
[3] O’Dricscoll, G., “The Essential Guide to Home Networking Technologies”, Prentis Hall, 2001
[4] 한치문, 박광로, “디지털 홈네트워크 기술 표준 개론,” TTA, 진한, 2004
[5] 양재수, 전호인, “유비쿼터스 홈네트워킹 서비스”, 전자신문사, 2004
[6] 문경덕, “홈네트워킹 미들웨어”, 2001
[7] 손성용, “한국산업기술대 CEO 특강 자료”, 2004
[8] http://www.osgi.org
[9] http://www.upnp.org
[10] http://www.dlna.org
[11] http://www.havi.org
[12] http://www.jini.org

## Slide 115: Questions?
http://www.osgi.org
http://www.osgikorea.org
Thank You!
谢谢!
감사합니다